## Slide 1: Classification of bridges based on Linked Data and Semantic Web technology
Jan Erik Hoel, Trimble
Lars Wikstrøm, Triona

## Slide 2
Presentation of the E39 Bjørnafjorden project
Bjørnafjorden Open Live Centre (BOLC)
The structure of the classification system V440
Why use Linked Data/Semantic Web technology (LD/SW)
Extremely brief introduction to LD/SW
How V44 is modelled with LD/SW technology
The way forward
Agenda

## Slide 3
E39 Bjørnafjorden project

## Slide 4
Selected concept
E39 Bjørnafjorden project

## Slide 5
E39 Bjørnafjorden project
Key values
Chosen concept: Floating bridge with anchor cables, fixed at one side.
Cable-stayed bridge at one side
Total length: 5,5 km
Fjord depth: 550 m
About 100 000 ton steel
About 35 pontoons
Main span of the cable-stayed bridge: 450 m
Bridge tower height: 215
Free sailing clearance: 50 m
Estimated cost: 17 billion NOK
Municipality plan approved 2019
Assumed start constuction 2024, finished 2028
Cost risks
Marked (steel)
Logistics

## Slide 6
E39 Bjørnafjorden project
Data management ambitions
BIM-model: From CAD-layer based data to level 3 BIM-model
Document management system: - Integrated with the BIM-model - Easy to search and find all relevant documentation
Seamless data transfer from design and build models (PIM) to asset management models (AIM)
Dashboard solution: Bjørnafjorden Open Live Centre (BOLC)

## Slide 7
E39 Bjørnafjorden – Open Live Centre (BOLC)
Design
BIM-server
Operate
Document Management
Databases
Open Live Centre
Project management tool for the E39 Bjørnafjorden project
Plan
Build
Maintain

## Slide 8
E39 Bjørnafjorden – Open Live Centre (BOLC)
Functionality examples for Open Live Centre (BOLC):
Extract and present data from the BIM-server
Harvest and publish data from different sources, like:
  Quantities
  Collisions and constructability
  Cost / Compensations
  Status / Progress
  Logistics
  RFID-sensors/ QR-code readings
  HR-data
  Environmental data
  Surveillance camera
  Visualisation / Animation
  Etc.

## Slide 9
Nordlenningen
*****************
Log In
Notes: Kongstanken – et LIVE center:
Høster data fra BIM-serveren – en dynamisk kobling
Også data fra andre kilder som overvåkningskamera, og data fra sensorer som strekklapper
- Logistikk - Kostnader - Kompensasjon - Visualiseringer - Kollisjoner - Mengder og antall - Analyser
- Status/fremdrift

## Slide 10
Notes: Kongstanken – et LIVE center:
Høster data fra BIM-serveren – en dynamisk kobling
Også data fra andre kilder som overvåkningskamera, og data fra sensorer som strekklapper
- Logistikk - Kostnader - Kompensasjon - Visualiseringer - Kollisjoner - Mengder og antall - Analyser
- Status/fremdrift

## Slide 11
V440 - The Norwegian Road Authority’s manual for bridge registration
The main purpose of the manual is to provide guiding for the personnel who do the registration and condition-monitoring of the bridges on the main road network in Norway.
The manual contains registration process descriptions and rules for bridge document management.
In addition the manual provides a comprehensive list of definitions of bridge types and bridge parts, that is bride classification.

## Slide 12
Bridge Categories:
V440 - The Norwegian Road Authority’s manual for bridge registration
Examples of bridge classification:
Code Description
1 Road bridge
2 Bridge embedded in the road superstructure
3 Pedestrian bridge
4 Ferry landing
6 Tunnel
7 Supportive structures
8 Railroad bridge
9 Other structures

## Slide 13
Bridge Types:
Beam bridges:
Concrete beam bridge
Steel beam bridge
Box bridge
Multiple box bridge
Box bridges:
Examples of bridge classification:

## Slide 14
Arc bridges:
Truss bridges:
Bridge Types:
Examples of bridge classification:
Arc bridge with upper carriageway
Arc bridge with lower carriageway
Truss bridge with upper carriageway
Truss bridge with lower carriageway

## Slide 15
Main Groups of Bridge Element Codes:
Examples of bridge classification:
Code Description
B Ground
C Substructure
D Superstructure
E Bridge Deck
F Structure embedded in filling
H Equipment

## Slide 16
Detailed Bridge Element Codes:
Examples of bridge classification:

## Slide 17
Why use Linked Data and Semantic Web (LD/SW) for BOLC
Why use LD/SW technology:
BOLC is an integration project. An integration project needs a common data model to be able to interpret and accumulate data
LD/SW is an extremely flexible technology for data modelling of different domains and combining these domains
The LD/SW technology is mature based on a well-developed standardisation work from international bodies like World Wide Web Consortium (W3C) and ISO
By using LD/SW technology as the back-bone of the integration architecture, we’ll facilitate an extremely flexible integration solution.
Why use V440 – Norwegian Bridge classification system :
For integration projects, it is crucial to have a common understanding of the domains
V440 provides a fully developed data model/ classification system for the main domain for this integration project
V440 is relevant for Norwegian conditions
V440 will be the “centre ontology” for the integration work, like the Core EUROTL on the next slide

## Slide 18
Interlink - EUROTL

## Slide 19: Linked Data & The Semantic Web – Crash course (5 mins)
http://www.w3.org/standards/semanticweb/

## Slide 20: Linked data – starting with the web (linked documents) Physical machines abstracted away
URL
URL
URL
URL

## Slide 21: Linked data - Semantic Web (Web of data)

## Slide 22: Basic concepts
RDF Resource Description Framework
RDFS – One level up
Resource Description Framework Schema
SPARQL
SPARQL Protocol and RDF Query Language
GeoSparQL
Ontologies OWL == Web Ontology Language

## Slide 23: Technology Stack – Web technology

## Slide 24: Basic Concepts
RDF – Resource Description Framework

## Slide 25: Basic Concepts

## Slide 26: Basic Concepts
RDFS – RDF Schema

## Slide 27: Basic Concepts
SPARQL – Querying the semantic web
SELECT ?wall ? Window
WHERE {
?wall rdf:type ont:Wall .
?wall ont:hasWindow ?window .
}

## Slide 28: Basic Concepts
OWL – Ontologies (RDFS++)
Web Ontology Language
OWL includes RDFS plus much more:
  E.g. Class “Mother” is the intersection of classes “Parent” and “Woman”
  E.g. My class “Wall” is equivalent to the class “IfcWall”
  E.g. System-A:BridgeA is the same as System-X:BridgeX
  OWL gives you a much larger vocabulary to play with =>It makes it easy to say anything you might want to say about your data =>OWL allows you to easily express the relationships between different ontologies using a standard annotation framework.
Semantic reasoning
  Inferring new triples (knowledge) from existing triples
  E.g. This individual belongs to “Parent” and “Woman” => Must be a “Mother”

## Slide 29
Use cases
Make structure explicit and readable/understandable by machines/applications
  RDF, RDFS, OWL
Referenceable from other standards/formats such as IFC & *GML
  Through the use of de-referenceable URI:s
Easily ”mappable” to other structures
  Through ”Linking Rule Sets”, i.e. ontologies of their own right, specifying schema level relationships
Available through standard Web API:s
  http GET, SPARQL endpoint
For free:
  Exchange format for both schema and data (XML, Json, Turtle, …)

## Slide 30
Inspiration from ISO 12006-2 Building construction — Organization of information about construction works — Part 2: Framework for classification
Construction complex
  aggregate of construction entities serving at least one user activity or function
Construction entity
  an independent unit of the built environment with a characteristic spatial structure, serving at least one user activity or function
Construction Entity part
  constituent of a construction entity
Construction element
  constituent of a construction entity with a characteristic technical function, form or position
Construction process
  process which uses construction resources to achieve construction results

## Slide 31
Use of CEN/TC442 Semantic Modelling and Linking Standard - Including the basicsemantics ontology

## Slide 32
Basic concepts used in RDF, RDFS and OWL
URI:s identify each concept
Define the concepts using owl:Class
Define relationships between classes using
  rdfs:subClassOf (for the taxonomy)
  basicsemantics:hasPart (for the meronomy with restrictions)
  And other owl:ObjectProperty if needed
Define the properties using owl:DatatypeProperty
Connect properties and classes with restrictions (cardinality, type)
  rdfs:domain, rdfs:range and/or owl:Restriction
Define Annotation using owl:AnnotationProperty
  E.g. capture the ”Codes” used in V440

## Slide 33
A challenge
The handbook defines a hierarchical structure of classes/codes, but
  It is not always strict with regards to the nature of the hierarchy
  E.g. taxonomies vs meronomies
rdfs/owl needs to support reasoning and to be ”semantically strict”
  A class is a set
  rdfs:subClassOf specifies a subset (used for taxonomies)
Example: Pillar
  In V440 there is no clear difference beteen
    The relationship between BuildingElement vs Pillar (is-a)
    And the relationship between Pillar and Foundation (has-a)

## Slide 34
The process
Define principles
Verify principles with domain experts
Define Excel structure
Bulk input from domain experts
Convert excel to rdf (generic spreadsheet structure)
Generate V440 ontology using SPARQL/SPIN
Verification
Validation

## Slide 35
composition
Ontology
composition
Construction entity
Construction entity part
Construction element
Properties

## Slide 36
Example dataset
dataset_test:Brudekke_E_1 rdf:type v440_1:Brudekke_E ; . dataset_test:Peler_B2_1 rdf:type v440_1:Peler_B2 ; . dataset_test:Platebru_massiv_21_1 rdf:type v440_1:Platebru_massiv_21 ; v440_1:harElement dataset_test:Brudekke_E_1 ; v440_1:harElement dataset_test:Peler_B2_1 ; v440_1:harStatisktSystem v440_1:Statisk_system_Kontinuerlig ; . dataset_test:Vegbru_1_1 rdf:type v440_1:Vegbru_1 ; v440_1:harDel dataset_test:Platebru_massiv_21_1 ;

## Slide 37
The way forward
An ontology (OTL) for V440 will be finished and published before March 2020
Further work on Linked Data Sets (LDS) to other relevant OTLs (IFC e.g.) will probably start in the spring 2020
The public tender for implementation of BOLC will be issued in Q1 2020
Software vendors will be invited to an “interoperate” from mid-April to the end of June 2020
  The purpose is to prototype the integration of LD/SW technology and the V440 OTL in relevant software products
  Will be arranged as facilitated workshops with independent work sessions in between
Information about this project, the LD/SW technology and the developed ontologies will be given to the industry in breakfast meetings, newsletters, seminars etc. It is important to get the industry engaged.