## Slide 1: V440 / V441 Klassifisering av bruer basert på Lenkede data og Semantisk Web teknologi
Jan Erik Hoel, buildingSMART Norge
Lars Wikström, Triona AB
https://www.youtube.com/watch?v=Ms8frmt2jD4

## Slide 2: Agenda
Hva inneholder V440 og V441?
Kort introduksjon til Lenkede Data og Semantisk Web (LD/SW)
Forankring i standarder
Hvorfor lage ontologier for V440/ V441?
Prosessen fram mot en V440 ontologi
Hvordan får jeg tak i ontologiene?

## Slide 3
V440 / V441- Statens vegvesen sine håndbøker for buregistrering og inspeksjon

## Slide 4
Brukategorier:
Eksempler på bruklassifisering:
Kode Beskrivelse
1 Vegbru
2 Bru i fylling
3 Gang- og sykkelvegbru
4 Ferjeleie
6 Tunnel
7 Støttekonstruksjoner
8 Jernbanebru
9 Annen byggverkskategori
V440 – Statens vegvesens håndbok for bruregistrering

## Slide 5
Brutyper:
Bjelkebru:
Bjelkebru med rektangulære betongbjelker
Bjelkebru med I-bjelker I stål
Kassebru med to steg
Kassebru med fire steg
Box bridges:
V440 - Eksempler på bruklassifisering:

## Slide 6
Buebruer:
Fagverksbruer:
Brutyper:
Buebru med overliggende brudekke
Buebru med underliggende brudekke
Parallellfagverksbru med oveliggende brudekke
Parallellfagverksbru med underliggende brudekke
V440 - Eksempler på bruklassifisering:

## Slide 7
Hovedgrupper av elementkoder:
Kode Beskrivelse
B Grunnen
C Underbygning
D Overbygning
E Brudekke/slitelag
F Konstruksjon I fylling
H Utstyr
V440 - Eksempler på bruklassifisering:

## Slide 8
Detaljerte elementkoder:
V440 - Eksempler på bruklassifisering:

## Slide 9
V441 - Eksempler skadelokalisering:

## Slide 10
V441 - Eksempler skadetyper:

## Slide 11
V441 - Eksempler på skadegrad, skadekonsekvens og skadeårsak:

## Slide 12
V441 UML-diagram

## Slide 13: Linked Data & The Semantic Web
http://www.w3.org/standards/semanticweb/
V441
V440

## Slide 14: Webben (“web av lenkede dokument”)
URL
URL
URL
URL

## Slide 15: Linked data - Semantic Web (“web av data”)

## Slide 16: Technology Stack – Web technology

## Slide 17: Basic concepts
RDF
Resource Description Framework
RDFS
Resource Description Framework Schema
SPARQL
SPARQL protocol and RDF Query Language
OWL
Web Ontology Language

## Slide 18: Basic Concepts
RDF – Resource Description Framework
A Fact!

## Slide 19: Basic Concepts

## Slide 20: Basic Concepts
RDFS – RDF Schema

## Slide 21: Basic Concepts
SPARQL – Querying the semantic web
SELECT ?wall ? Window
WHERE {
?wall rdf:type ont:Wall .
?wall ont:hasWindow ?window .
}

## Slide 22: Basic Concepts
Mother
OWL – Ontologies (RDFS++)
Web Ontology Language
OWL includes RDFS plus much more:
  E.g. Class “Mother” is the intersection of classes “Parent” and “Woman”
  E.g. My class “Wall” is equivalent to the class “IfcWall”
  E.g. System-A:BridgeA is the same as System-X:BridgeX
  OWL allows you to easily express the relationships between different ontologies using a standard annotation framework.
Semantic reasoning
  Inferring new triples (knowledge) from existing triples
  E.g. This individual belongs to “Parent” and “Woman” => Must be a “Mother”
Woman
Parent
rdf:type
rdf:type
rdf:type

## Slide 23: EUROTL: Eksempel på «Linking Rule Sets»

## Slide 24: LD/SW – Videre lesing
W3C - OWL language guide
Intro
5 star open data
Semantic web for dummies
Programming the semantic web
Linked Open Vocabularies
Protégé pizza tutorial
DBPedia SPARQL endpoint
Linked Geodata
  SPARQL Endpoint
LinkedDataHub

## Slide 25
Inspiration från ISO 12006-2 Building construction — Organization of information about construction works — Part 2: Framework for classification
Construction complex
  aggregate of construction entities serving at least one user activity or function
Construction entity
  an independent unit of the built environment with a characteristic spatial structure, serving at least one user activity or function
Construction Entity part
  constituent of a construction entity
Construction element
  constituent of a construction entity with a characteristic technical function, form or position
Construction process
  process which uses construction resources to achieve construction results
V440 handler egentlig om klassifikasjon!

## Slide 26
Pilot for CEN/TC442 Semantic Modelling and Linking Standard - Inklusive ontologin basicsemantics-owl
How to model
  LoC 1 – Terminology & definitions alignment
    Vocabulary/Thesaurus
  LoC 2 – Data exchange/sharing
    Ontology Open World
  LoC 3 – Data integration
    Ontology Closed World
  Naming conventions
  Decomposition
  Quantity kind & Units
  Quantity modelling
  Conceptual (top level) modelling
How to link
  LoC 1 – Weak linking
  LoC 2 – Medium linking
  LoC 3 – Strong linking

## Slide 27
hasPart
V440 Ontologien
hasPart
Construction entity (=Byggverkskategori)
Construction entity part (=Byggverkstype)
Construction element (=Byggverkselement)
Properties (=Kap. 7 – Brudata)

## Slide 28
Hvorfor ontologier for V440 / V441?
Gjør strukturen og innholdet i V440/ V441 maskinlesbart
  Benytter RDF, RDFS, OWL som REPRESENTATION men beholder innholdet
Gjør strukturen direkte refererbar fra andre standarder og format som f.eks. IFC og GML
  Gjennom å bruke URI:er for identifikasjon
Gir mulighet for å mappe mot begrep i andre standarder
  Gjenom å bruke standardisert semantik (W3C) i ”Linking Rule Sets”/”Alignment ontologies”, dvs. Separate ontologier som spesifiserer relasjoner mellom konsept på skjema-nivå.
Tilgang via standardiserede WEB-API’er
  http GET, SPARQL endpoint
”På kjøpet”:
  Åpne dataformat for både skjema og data (XML, Json, Turtle, …)

## Slide 29
Prosessen
Domain Experts
Linked Data and Semantic Web Experts
Project Mangement
TopBraid Composer
Project Sponsor
Software Vendors
NPRA
NPRA
NPRA
V440 spreadsheets
V440 ontologies
Published V440 ontologies
Server Administrator
ttl/SPARQL
ttl/SPARQL
ttl/SPARQL
ttl/SPARQL
Project Phase One
Project Phase Two
Project Phase Three
xlsx-file
manually
ttl
IFC BIM-model
IFC BIM-model
IFC BIM-model
Rendra
IFC BIM-model
Interested Stakeholders
Classification part of V440

## Slide 30
Hvor får jeg tak i V440 (og etterhvert V441) ontologiene
Offisiell Svv side for V440 ontologien: https://www.vegvesen.no/fag/teknologi/bruer/bruhandboker/v440-maskinlesbar-bim
V440 SPARQL endpoint: http://rdfspatial.vegdata.no:7200/repositories/V440 V440 Prosjektside: https://github.com/buildingsmart-norway/maskinlesbar_v440